Brief Grace Package Manager Specification

'a lamb to the slaughter'

I	BASIC CONCEPTS

Package in grace:

A bundle of .grace/.gcn/.gso files together with a package descriptor.

(Does a downloaded package need to be compiled, or should it not bother considering	minigrace will do this anyway? This ties into the /bin /src folder issue – perhaps low priority.)

II	OVERVIEW

Grace Package Manager to be a standalone command line tool (and may GUI in future).	Gpm can be given a range arguments:

gpm list	- lists currently installed packages
gpm install [package url]	- installs package from specified url
gpm update [package url]	- updates package from specified url
gpm bundle	- generates package and package descriptor
gpm help	- lists command line arguments

III	SPECIFIC FUNCTIONALITY

A.	Install Package

Example:

gpm install github.com/coolpackage/cool.tar.gz

Steps:

1. Download and unpack tarball (curl/gzip – Question here about Windows compatibility...)
2. Package descriptor file required to be in package tarball. Package descriptor (.gpm file) includes information such as package name and verbose name (verbose name is url), version, dependencies, (checksum etc).
3. If new package, unpack package into usr/lib/grace/[PACKAGE NAME] where the package name is defined by the package descriptor.
Evaluates package descriptor to determine additional dependencies. Downloads and installs dependencies.
1. If package exists, and downloaded tarball is of a different version, prompt user with choice to update package to new version. See 'update' section.
2. Update local package mapping file with new package information. Mapping will be, for example:

github.com/coolpackage/	cool
github.com/notcool/	notcool

If there is a naming conflict (e.g. package called 'cool' already exists) the package manager requests a new name for the package mapping or uses the package's verbose name.

B.	Update Package

i.	Update Specific Package
Example:

%gpm list
> 1 installed package(s):
>	cool	github.com/coolpackage/cool.tar.gz	v.1.1.0
%gpm update cool
> Updating...
>	Resolving url
>	Downloading version 1.1.1
>	Installing version 1.1.1
> Package 'cool' has been updated from v.1.1.0 to v.1.1.1

Steps:

1. Resolve package according to local mapping. Download tarball and determine whether version is up to date according to .gpm descriptor file.
2. If package not up to date:
  - Remove existing package
  - Install new package.
  - Download and install all listed dependencies of new package.

ii.	Update All Packages

Example:

%gpm update all

Steps:

Updates all packages specified in package mapping.

C.	Bundle Package

Example:

%gpm bundle /usr/newPackage [PACKAGE NAME] [VERSION]

Steps:

1. Creates .gpm package manager descriptor file .grace files in a given directory.
2. Can create tarball.
3. ??
4. Do we want this?

D.	Package Descriptors

Tim provided us with an example of what these would look like and discussed writing a	dialect to process these. What would such a dialect look like, and is this necessary/desired?
Alternatively, we could simply have a basic text file that includes some package meta-data	in an easy to process format (perhaps json or xml, or just key words and values).